Introduction to x86
Ivan Sorokin

---
Computer Model
A real computer is a complicated piece of hardware with many intricate details. For teaching purposes we will leave out some unnecessary details. Initially we will discuss a simplified model suitable for teaching. Later we will refine our model to match real hardware more closely.

---
Computer Model
In a (highly) simplified model a computer consists of two components a CPU and RAM
CPU
RAM
read
write

---
RAM
RAM (Random Access Memory) is a numbered set of cells.
#135
#136
#137
#138
#139
#141
#134
#140
…
65
6C
6C
6F
20
6F
…
68
77
Numbered means that each cell has a number assigned to it.
The total number of cells determines the amount of RAM. As of 2016 computers typically have 8GB-32GB of RAM installed.
(TODO) In our model we will assume that cells are number from 0 to N. This is not the case in real world, where valid ranges can be non-continous.

---
RAM
#135
#136
#137
#138
#139
#141
#134
#140
…
65
6C
6C
6F
20
6F
…
68
77
RAM supports two operations: read and write.
- write, given a cell index and a value, changes the content of the specified cell to the specified value. Cell retain its content till the next write to the same cell
- read, given a cell index, retrieves the content of the specified cell
The index of a cell is called an address.
A cell can be modified only as a whole e.g. individual bits in a cell can not be modified independently.

---
RAM
In our model we will assume cell size to be 1 byte.
(sidenote) In the real world, data between a CPU and RAM is never transfered in bytes, as the overhead of transfering individual bytes gets prohibitely large. Modern RAM has a single addressable unit 64 bytes long which is of the same size as a cache line of modern CPUs. As the CPU maintains an illusion that memory can be byte-addressable we will ignore this detail for now.

---
CPU
A CPU executes programs.
A CPU keeps an internal number called register IP (instruction pointer). This register holds the address of the next instruction to be executed. On each step it reads a byte at address IP and possibly several following bytes. Each sequence of bytes is called an instruction and has a meaning assigned. CPU executes the instruction then add the length of the command to the register IP so the next instruction will be executed on the next step.

---
CPU
Step #1
IP=137
#135
#136
#137
#138
#139
#141
#134
#140
01
D8
89
D3
49
F7
…
C2
75
…
Step #2
IP=139
#135
#136
#137
#138
#139
#141
#134
#140
01
D8
89
D3
49
F7
…
C2
75
…
Step #3
IP=140
#135
#136
#137
#138
#139
#141
#134
#140
01
D8
89
D3
49
F7
…
C2
75
…
This process repeats billions times a second. Modern CPUs are able to execute up to 12 billion instructions a second.

---
CPU
For convenience instructions are typically written not in their memory encoding, but using a human-readable mnemonics. E.g.
89 C2 mov dx,ax
01 D8 add ax,bx
89 D3 mov bx,dx
49 dec cx
75 F7 jnz mylabel
The language of these mnemonics is called Assembly Language.

---
CPU
1. In addition to register IP, x86 CPU has 8 so-called GPRs (general purpose registers). Their names are:
2. AX, CX, DX, BX, SP, BP, SI, DI
3. These registers are 16-bit wide.
5. A register is a (very fast) memory cell located in a CPU. Most arithmetic operations operate on GPRs. GPRs are commonly used to keep intermediate results of computation.

---
Instruction MOV
1. The simplest and one of the most commonly used insturuction on x86 is MOV. MOV has two arguments source and destination. It copies the value from source to destination. Destination can be a register and source can be another register or an immediate value.
2. MOV dst, src ; dst = src
3. B8 05 00 MOV AX, 5 ; AX = 5
4. B9 0A 00 MOV CX, 10 ; CX = 10
5. 89 C8 MOV AX, CX ; AX = CX
6. 89 D0 MOV AX, DX ; AX = DX
7. 89 CA MOV DX, CX ; DX = CX

---
Instruction MOV
1. MOV can be used to move values to/from memory. Brackets are used to refer to memory location.
2. ; read 10th memory cell to register AX
3. A1 0A 00 MOV AX, [10]
4. ; read the memory cell with index BX to AX
5. 8B 07 MOV AX, [BX]
6. ; write AX to the memory cell with index BX
7. 89 07 MOV [BX], AX

---
Endian
#135
#136
#137
#138
#139
#141
#134
#140
…
65
6C
AA
6F
20
6F
…
68
77
1. MOV AX, [136]
3. What value will be stored in AX?
- 43628 (0xAA6C) — little endian (x86)
- 27818 (0x6CAA) — big endian

---
8-bit memory operations
#135
#136
#137
#138
#139
#141
#134
#140
…
65
6C
AA
6F
20
6F
…
68
77
1. One can read a single byte of memory by using 8-bit registers (AL, AH, BL, BH, CL, CH, DL, DH):
   MOV AL, [136]
3. 108 (0x6C) will be stored in AL.

---
Registers 16-bit
15 … 8
7 … 0
15 … 0
AX
SP
AH
AL
BX
BP
BH
BL
CX
SI
CH
CL
DX
DI
DH
DL
8 bit
8 bit
16 bit
16 bit

---
Instruction MOV
1. Not all combinations of sources and distinations are allowed. For example a single MOV instruction can not move data from memory to memory.
2. $ cat 1.asm
3. mov [ax], [bx]
4. $ nasm 1.asm
5. 1.asm:1: error: invalid combination of opcode and operands

---
Instruction MOV
1. A set of valid combinations of sources and destinations was expanding over time. On modern CPUs it includes:
2. MOV reg, reg
3. MOV reg, imm
4. MOV reg, [imm]
5. MOV reg, [reg]
6. MOV [reg], reg
7. MOV [reg], imm
8. MOV [imm], reg
9. MOV [imm], imm

---
Basic Arithmetic Instructions
1. A set of basic arithmetic instructions includes instructions: ADD, SUB, AND, OR, XOR
2. ; ADD writes to the destination the sum of the
3. ; source and the destination
4. 01 C8 ADD AX, CX ; AX = AX + CX
5. ; SUB writes the difference, ditto AND, OR, XOR
6. 29 C8 SUB AX, CX ; AX = AX - CX
7. 21 C8 AND AX, CX ; AX = AX & CX
8. 09 C8 OR AX, CX ; AX = AX | CX
9. 31 C8 XOR AX, CX ; AX = AX ^ CX

---
Basic Arithmetic Instructions
1. ADD, SUB, AND, OR, XOR supports the same source/destination combinations as MOV:
3. 21 D8 AND AX, BX
4. 83 E0 05 AND AX, 5
5. 23 06 05 00 AND AX, [5]
6. 23 07 AND AX, [BX]
7. 21 07 AND [BX], AX

---
INC, DEC
INC (increment), DEC (decrement) have only one argument:
2. 40 INC AX
3. FE 07 INC byte [BX]
4. FF 07 INC word [BX]
5. 48 DEC AX

---
NEG, NOT
NEG (negate), NOT (bit-wise not):
2. F7 D8 NEG AX
3. F6 1F NEG byte [BX]
4. F7 1F NEG word [BX]
5. F7 D0 NOT AX

---
MUL, DIV
The format of MUL and DIV instructions differs from the one of other arithmetic instructions. MUL has only one argument. It multiply AX by its argument and write the result to a pair DX:AX, where DX is high part and AX low part.
1. MUL src ; DX:AX = AX * src
F7 E3 MUL BX ; DX:AX = AX * BX
F7 27 MUL WORD [BX] ; DX:AX = AX * [BX]
1. There are two types of MUL instructions. One for unsigned value (MUL) and one for signed (IMUL).
2. F7 EB IMUL BX ; DX:AX = AX * BX

---
DIV
Division has a signed (IDIV) and an unsigned (DIV) forms. They divides a number represented by a pair of registers DX:AX, where DX is high part and AX is low part by the argument. The quotient is written to AX, the remainder to DX.
2. DIV src ; AX = DX:AX / src
3. ; DX = DX:AX % src
1. F7 F3 DIV BX ; AX = DX:AX / BX
2. ; DX = DX:AX % BX
3. F7 FB IDIV BX ; AX = DX:AX / BX
4. ; DX = DX:AX % BX

---
CWD
1. In case a division of a 16-bit number by a 16-bit number is required, 16-bit divident need to be expanded to 32-bit pair DX:AX. For unsigned numbers we just need to zero out high half.
2. 31 D2 XOR DX,DX ; zero out dx
3. F7 F3 DIV BX
4. For signed special instruction CWD exists to copy the highest bit of AX to all bits of DX.
5. 99 CWD
6. F7 FB IDIV BX

---
CWD
1. CWD converts 16-bit value in AX to 32-bit value in DX:AX.
3. 99 CWD
4. F7 FB IDIV BX
6. This operation is called
7. “signed extension”.
AX (16-bit)
F840
= -1984
DX:AX (32-bit)
FFFFF840
= -1984
AX (16-bit)
1
1
1
1
1
0
...
0
= -1984
DX:AX (32-bit)
1
1
1
1
1
1
...
1
1
1
1
1
1
0
...
0
= -1984

---
DIV
1. In case a division by zero is requested. The execution of the program is interrupted and the control is transferred to the OS. It is up to the OS to decide what to do with the program next. The program is usually terminated. Most OSes provide a (OS-specific) way to handle the division by zero and to continue the execution.
2. When the result of 32-bit by 16-bit division doesn’t fit 16-bit register the same error as division by zero is reported.

---
Shifts
1. For shifts there are three instructions available:
2. D3 E0 SHL AX,CL
3. D3 E8 SHR AX,CL
4. D3 F8 SAR AX,CL

---
Shifts
SHL AX,3
SHR AX,3
15
15
0
0
1
1
1
1
1
0
0
0
1
0
0
0
1
1
1
0
1
1
1
1
1
0
0
0
1
0
0
0
1
1
1
0
1
1
0
0
0
1
0
0
0
1
1
1
0
0
0
0
0
0
0
1
1
1
1
1
0
0
0
1
0
0
0
1
SAR AX,3
1. SHR is called logical shift. It is used for unsigned numbers.
3. SAR is called arithmetic shift. It is used for signed numbers.
15
0
1
1
1
1
1
0
0
0
1
0
0
0
1
1
1
0
1
1
1
1
1
1
1
1
0
0
0
1
0
0
0
1

---
Branches, JMP
1. Instruction JMP modify register IP, so the next instruction to be executed is not the next instruction after JMP, but the instruction at the address specified in the argument.
2. 40 loop: INC AX
3. EB FD JMP loop
4. FD means -3. It is added to register IP after execution of JMP instruction. It means that targets of 2-byte JMP instruction must be within range -128..127 from the end of JMP instruction.

---
JMP
1. In case JMP target is further than -128..127 then longer form of JMP can be used.
2. E9 34 12 JMP label
4. ... 0x1234 bytes of data
6. label:

---
Conditional Branches
1. To make a conditional branch a pair of instructions is required:
3. 39 D8 cmp ax, bx ; compare ax and bx
4. 74 10 je label ; jump if ax == bx
6. 39 D8 cmp ax, bx ; compare ax and bx
7. 7F 10 jg label ; jump if ax > bx

---
Conditional branches
There are many types of conditional branches:
2. je, jne jump if equal/not-equal
3. jg, jng jump if greater (signed)
4. jl, jnl jump if less (signed)
5. ja, jna jump if above (unsigned)
6. jb, jnb jump if below (unsigned)

---
FLAGS register
1. cmp instruction modifies the register called FLAGS.
2. jxx instructions reads register FLAGS and jump according to the condition.
5. Bits from this register have they own names:
- bit C is called carry flag
- bit Z is called zero flag
- bit S is called sign flag
- bit O is called overflow flag
15
0
0
0
0
0
O
D
I
T
S
Z
0
A
0
P
1
C

---
Conditional branches
1. There are jxx instructions that checks the specific bits in FLAGS register.
3. jc/jnc jump if carry flag is set
4. jz/jnz jump if zero flag is set
5. js/jns jump if sign flag is set
6. jo/jno jump if overflow flag is set

---
FLAGS register
1. Register FLAGS is modified not only by instruction CMP, but also by most other arithmetic instructions (ADD, SUB, MUL, etc).
2. CMP modifies register FLAGS the same way SUB instruction does (CMP is SUB that doesn’t write destination).
3. ADD/SUB modify FLAGS register in the following way:
- ZF (zero) is set when the result is zero.
- SF (sign) is set when the result is negative.
- CF (carry) is set when unsigned operation caused 16th bit to be carried over/borrowed from
- OF (overflow) is set when signed operation causes overflow.

---
Carry Flag vs Overflow Flag
1. 0000 + 0001 = 0001
2. signed 0 + 1 = 1
3. unsigned 0 + 1 = 1
4. OF = 0 CF = 0
1. 7FFF + 0001 = 8000
2. signed 32767 + 1 = -32768
3. unsigned 32767 + 1 = 32768
4. OF = 1 CF = 0
1. FFFF + 0001 = 0000
2. signed -1 + 1 = 0
3. unsigned 65535 + 1 = 0
4. OF = 0 CF = 1
1. 8000 + 8000 = 0000
2. signed -32768 + -32768 = 0
3. unsigned 32768 + 32768 = 0
4. OF = 1 CF = 1

---
CMP vs SUB
sub AX, BX
- ZF (zero) is set when the result is zero.
- SF (sign) is set when the result is negative.
- CF (carry) is set when unsigned operation caused 16th bit to be carried over/borrowed from
- OF (overflow) is set when signed operation causes overflow.
1. cmp AX, BX
2. je label
4. Which flag je should check?

---
CMP vs SUB
sub AX, BX
- ZF (zero) is set when the result is zero.
- SF (sign) is set when the result is negative.
- CF (carry) is set when unsigned operation caused 16th bit to be carried over/borrowed from
- OF (overflow) is set when signed operation causes overflow.
1. cmp AX, BX
2. je label
4. Which flag je should check?
6. Answer: ZF.
8. 74 10 je label
9. 74 10 jz label
10. je and jz is the same instruction!

---
Conditional branches
1. There are jxx instructions that checks the specific bits in FLAGS register.
3. je/jz jump if ZF=1
4. jc jump if CF=1
5. js jump if SF=1
6. jo jump if OF=1

---
CMP vs SUB
sub AX, BX
- ZF (zero) is set when the result is zero.
- SF (sign) is set when the result is negative.
- CF (carry) is set when unsigned operation caused 16th bit to be carried over/borrowed from
- OF (overflow) is set when signed operation causes overflow.
1. cmp AX, BX
2. ja/jb label
4. Which flag ja/jb should check?

---
Conditional branches
1. There are jxx instructions that checks the specific bits in FLAGS register.
3. je/jz jump if ZF=1
4. jb/jc jump if CF=1
5. ja jump if CF=0 & ZF=0
6. js jump if SF=1
7. jo jump if OF=1

---
CMP vs SUB
sub AX, BX
- ZF (zero) is set when the result is zero.
- SF (sign) is set when the result is negative.
- CF (carry) is set when unsigned operation caused 16th bit to be carried over/borrowed from
- OF (overflow) is set when signed operation causes overflow.
1. cmp AX, BX
2. jg/jl label
4. Which flag jg/jl should check?

---
Flags Graph
1. CMP AX, BX
BX
215-1
-215
AX
215-1
-215

---
Flags Graph
1. CMP AX, BX
BX
215-1
ZF=1
-215
AX
215-1
-215

---
Flags Graph
1. CMP AX, BX
BX
SF=1
215-1
ZF=1
-215
AX
215-1
-215

---
Flags Graph
1. CMP AX, BX
BX
SF=1
215-1
ZF=1
-215
AX
215-1
-215

---
Flags Graph
1. CMP AX, BX
BX
SF=1
215-1
ZF=1
-215
AX
215-1
-215

---
Flags Graph
1. CMP AX, BX
BX
SF=1
215-1
-215
AX
215-1
-215

---
Flags Graph
1. CMP AX, BX
BX
BX
SF=1
OF=1
215-1
215-1
AX
-215
215-1
-215
-215

---
Flags Graph
1. AX < BX
BX
BX
SF=1
OF=1
215-1
215-1
AX
-215
215-1
-215
-215

---
Conditional branches
1. There are jxx instructions that checks the specific bits in FLAGS register.
3. je/jz jump if ZF=1
4. jb/jc jump if CF=1
5. ja jump if CF=0 & ZF=0
6. jl jump if SF≠OF
7. jg jump if SF=OF & ZF=0
8. js jump if SF=1
9. jo jump if OF=1

---
Branches
1. Many instructions update FLAGS register according to the result of the operation. Sometimes conditional branches can be made without cmp:
2. 89 C2 loop: mov dx,ax
3. 01 D8 add ax,bx
4. 89 D3 mov bx,dx
5. 49 dec cx
6. 75 F7 jnz loop

---
Registers 32-bit
AX
EAX
AX
AH
AL
AH
AL
8 bit
8 bit
8 bit
8 bit
16 bit
16 bit
32 bit

---
Registers 32-bit
EAX
ESP
AX
SP
AH
AL
EBX
EBP
BX
BP
BH
BL
ECX
ESI
CX
SI
CH
CL
EDX
EDI
DX
DI
DH
DL

---
Registers 64-bit
RAX
EAX
AX
AH
AL
8 bit
8 bit
16 bit
32 bit
64 bit

---
Registers 64-bit
RAX
R8
EAX
R8D
AX
AX
R8W
R8B
AH
AL
RBX
R9
EBX
R9D
BX
R9W
R9B
BH
BL
RCX
R10
ECX
R10D
CX
R10W
R10B
CH
CL
RDX
R11
EDX
R11D
DX
R11W
R11B
DH
DL
RSP
R12
ESP
R12D
SP
R12W
SPL
R12B
RBP
R13
EBP
R13D
BP
R13W
BPL
R13B
RSI
R14
ESI
R14D
SI
R14W
SIL
R14B
RDI
R15
EDI
R15D
DI
R15W
DIL
R15B

---
Addressing modes
1. MOV reg, [reg + {1,2,4,8} * reg + imm]
3. 48 8B 44 8B 01 MOV RAX, [RBX + RCX*4 + 1]
4. 48 8D 44 8B 01 LEA RAX, [RBX + RCX*4 + 1]

---
ADC
1. ADD AX, BX
3. (17-bit) (16-bit) (16-bit)
4. CF:AX = AX + BX
6. ADC AX, BX
8. (17-bit) (16-bit) (16-bit) (1-bit)
9. CF:AX = AX + BX + CF

---
SBB
1. SUB AX, BX
3. (17-bit) (16-bit) (16-bit)
4. CF:AX = AX - BX
6. SBB AX, BX
8. (17-bit) (16-bit) (16-bit) (1-bit)
9. CF:AX = AX - BX - CF